## Slide 1: How to Use this Slide Deck
What’s Included?
  Instructional and exercise slides for the LabVIEW Student Ambassadors
  End of lesson quiz questions
  Exercises that are designated “Homework” exercises
What’s Excluded?
  Sections involving hardware
[Last Updated 08.20.2015]

## Slide 3: LabVIEW Core 1
Notes:   The slides from here to the first lesson slide are the standard front matter for any course. Any text in red should be replaced with text appropriate to your course.

## Slide 4
Course Learning Map
Welcome to LabVIEW Core 1
Lesson 1
Troubleshooting and Debugging VIs
Lesson 4
Lesson 2
Navigating LabVIEW
Creating Your First Application
Lesson 3
Using Loops
Lesson 5
Modularity
Lesson 6
Creating and Leveraging Data Structures
Using Decision-Making Structures
Lesson 7
Lesson 8
Using Sequential and State Machine Programming
Lesson 9
Acquiring Measurements with Hardware
Accessing Files in LabVIEW
Lesson 10
Notes:   <Replace text with your lesson titles. Click each smart art, press the left expand icon, and add or remove Lessons as needed. Resize the smart art to fit the actual number of lessons.>

## Slide 5
Lesson 8
Acquiring Measurements from Hardware
Understand how LabVIEW connects to hardware to get real-world measurements.
Measurement Fundamentals with NI DAQ Hardware
Automating Non-NI Instruments

## Slide 6
A. Measurement Fundamentals with NI DAQ Hardware
Recognize the components of a DAQ system and practice connecting to hardware.

## Slide 7
DAQ─Measuring Physical Phenomenon with a Computer
A. Measurement Fundamentals with NI DAQ Hardware

## Slide 8
Measurement Fundamentals with NI DAQ
DAQmx
LabVIEW

## Slide 9
Use NI MAX to examine and test a DAQ device.
Exercise 8-1
Using NI MAX to Examine a DAQ Device

## Slide 10
Exercise 8-1
Using NI MAX to Examine a DAQ Device

## Slide 11
3 Ways to Connect with a DAQ Device
A. Measurement Fundamentals with NI DAQ Hardware
NI MAX
DAQ Assistant
DAQmx API

## Slide 12
Explore a DAQmx example program that continuously acquires data and modify it to wait on a digital trigger.
Exercise 8-2
Programming with the DAQmx API

## Slide 13
Exercise 8-2
What types of VIs did you use outside of the While Loop?
Programming with the DAQmx API

## Slide 14
B. Automating Non-NI Instruments
Recognize the components of an instrument control system and practice connecting to hardware.

## Slide 15
LabVIEW controls instruments through different buses.
B. Automating Non-NI Instruments

## Slide 16
Automating Non-NI Instruments

## Slide 17
Use NI MAX to examine and communicate with an instrument using GPIB interface settings.
Exercise 8-3
Instrument Configuration with NI MAX

## Slide 18
Exercise 8-3
Instrument Configuration with NI MAX

## Slide 19
Simplify Instrument Control
B. Automating Non-NI Instruments
LabVIEW
Instrument Commands
(*idn?, meas?)
Bus Communication Protocol
(configure, read, write, trigger)
Instrument Driver

## Slide 20
Instrument Driver VIs for an Agilent Digital Multimeter
B. Automating Non-NI Instruments
Notes: This slide transitions to the next exercise.
The block diagram:
Initializes the Agilent 34401 digital multimeter (DMM)
Uses a configuration VI to choose the resolution and range
Selects the function
Enables or disables auto-range
Uses a data VI to read a single measurement
Closes the instrument
Checks the error status
You can locate most LabVIEW Plug and Play instrument drivers in the Instrument Driver Finder.
  Access within LabVIEW by selecting Tools» Instrumentation»Find Instrument Drivers or Help»Find Instrument Drivers.
  Use it to connect with ni.com to find instrument drivers.
  You can also find instrument drivers at ni.com/idnet
When you install an instrument driver, the installer:
  Adds an example program using the driver to the NI Example Finder.
  Adds instrument driver VIs to the Instrument I/O»Instrument Drivers palette in the Functions palette.
  Extracts instrument driver VIs and supporting files to the <LabVIEW>\instr.lib directory.

## Slide 21
Install an instrument driver and explore the example programs that accompany it.
Exercise 8-4
Exploring Instrument Drivers

## Slide 22
Exercise 8-4
How would you modify the example programs if you wanted to continuously acquire data?
Exploring Instrument Drivers

## Slide 23
Activity 8-1
Refer to the participant guide to answer questions about what you have learned in this lesson and then discuss the answers as a group.
Lesson Review

## Slide 24
What is NI MAX? (multiple answers)
A tool to configure and test DAQ devices
A tool to test instrument communication
A configurable Express VI
A window to view LabVIEW project files
Lesson Review
Notes:   Answer is a & b.

## Slide 25
What is NI MAX? (multiple answers)
A tool to configure and test DAQ devices
A tool to test instrument communication
A configurable Express VI
A window to view LabVIEW project files
Lesson Review
Notes:   Answer is a & b.

## Slide 26
Which of the following are benefits of instrument control? (multiple answers)
Automate processes
Improve productivity and repeatability
One platform for multiple tasks
Limited to only one type of instrument
Lesson Review
Notes:   Answer is a, b, and c.

## Slide 27
Which of the following are benefits of instrument control? (multiple answers)
Automate processes
Improve productivity and repeatability
One platform for multiple tasks
Limited to only one type of instrument
Lesson Review
Notes:   Answer is a, b, and c.

## Slide 28
VISA is a high-level API that calls low-level drivers.
True
False
Lesson Review
Notes: Answer is a.

## Slide 29
VISA is a high-level API that calls low-level drivers.
True
False
Lesson Review
Notes: Answer is a.

## Slide 30
Lesson 9 Accessing Files in LabVIEW
Describe the basic concept of file I/O and apply the appropriate File I/O functions to a given scenario.
Accessing Files from LabVIEW
High-Level and Low-Level File I/O Functions
Comparing File Formats

## Slide 31
A. Accessing Files from LabVIEW
Identify the steps for writing and reading files from a LabVIEW application.

## Slide 32
Typical File I/O Operations
A. Accessing Files from LabVIEW
Open/ Create/ Replace File
Read
and/or Write to File
Close
File
Check for
Errors
Notes: File I/O operations pass data to and from files. Use the File I/O VIs and functions to handle all aspects of file I/O.
A typical file operation involves the following process: Open/Initialize/Create -> Read/Write -> Close the reference -> Check for errors

## Slide 33
File I/O Palette for File Operation Functions
A. Accessing Files from LabVIEW

## Slide 34
B. High-Level and Low-Level File I/O Functions
Identify when to use high-level and low-level File I/O functions.

## Slide 35
High-Level File I/O
B. High-Level and Low-Level File I/O Functions
Open/ Create/ Replace File
Read
and/or Write to File
Close
File
Check for
Errors
Notes: High-level File I/O functions:
  Perform all three steps (open, read/write, close) for common file I/O operations.
  Might not be as efficient as the functions configured or designed for individual operations.
Write to Spreadsheet File
  Converts an array of double-precision numbers to a text string and writes the string to an ASCII file.
Read From Spreadsheet File
  Reads a specified number of lines or rows from a numeric text file and outputs a 2D array of double-precision numbers.
Write To/Read From Measurement File
  Express VIs that write data to or read data from an LVM or TDMS file format.

## Slide 36
Observe how a high-level file I/O VI writes to a spreadsheet-readable file.
Exercise 9-1
Exploring High-Level File I/O

## Slide 37
Exercise 9-1
How would you include more columns of data in the log file?
Exploring High-Level File I/O

## Slide 38
Low-Level File I/O
B. High-Level and Low-Level File I/O Functions
Open/ Create/ Replace File
Read
and/or Write to File
Close
File
Check for
Errors
Notes: A refnum is a temporary pointer to the resource

## Slide 39
File Refnums
Identify unique file I/O sessions.
B. High-Level and Low-Level File I/O Functions
refnum

## Slide 40
Streaming Data to Disk
B. High-Level and Low-Level File I/O Functions
Notes: Explain the concept of disk streaming here. Emphasize opening and closing the file outside of the loop.
Low-level File I/O functions:
  Provide individual functions for each step.
  Are efficient for writing to a file in a loop.

## Slide 41
String Functions
Convert data types to text
B. High-Level and Low-Level File I/O Functions
Notes: To write data to a text file, you must convert your data to a string. To write data to a spreadsheet file, you must format the string as a spreadsheet string, which is a string that includes delimiters, such as tabs.
Converting numeric and Boolean data types to strings and string operations basics

## Slide 42
Modify a VI to create an ASCII file using disk streaming.
Exercise 9-2
Temperature Monitor VI—Logging Data

## Slide 43
Exercise 9-2
What would happen if you used the Open/Create/Replace File and Close File functions inside the While Loop?
Temperature Monitor VI—Logging Data

## Slide 44
C. Comparing File Formats
Recognize different options for logging data to disk.

## Slide 45
Common Log File Formats
C. Comparing File Formats
Binary
ASCII/ LVM
TDMS
Notes: LabVIEW can use or create the following file formats:
Binary—Efficient, compact, and allows random access reading but not a human-readable file. Commonly used for high-speed and multi-channel DAQ.
ASCII—Human-readable text file where data is represented as strings. Commonly used for low-speed DAQ.
LVM—Format built on ASCII, the LabVIEW measurement data file (.lvm) is a tab-delimited text file you can open with a spreadsheet application or a text-editing application.
TDMS—An NI-specific binary file format that contains data and stores properties about the data.
ASCII files are also called text files.
Students will learn more about TDMS files in LabVIEW Core 2.

## Slide 46
Comparing File Formats
C. Comparing File Formats
 | ASCII | Binary | TDMS | LVM
Easily Exchangeable |  |  |  | 
Small disk footprint |  |  |  | 
Random read/write access |  |  |  | 
Inherent attributes |  |  |  | 
High-speed streaming |  |  |  | 
Notes: In this course, you learn about creating text (ASCII) files.
Use ASCII files in the following situations:
  You want to access the file from another application.
  Disk space and file I/O speed are not crucial.
  You do not need to perform random access reads or writes.
  Numeric precision is not important.

## Slide 47
Activity 9-1
Refer to the participant guide to answer questions about what you have learned in this lesson and then discuss the answers as a group.
Lesson Review

## Slide 48
After opening a file, which output does the Open/Create/Replace File I/O function return?
  File path
  File name
  Refnum out
  Task out
Lesson Review
Notes: Answer is c.

## Slide 49
After opening a file, which output does the Open/Create/Replace File I/O function return?
  File path
  File name
  Refnum out
  Task out
Lesson Review
Notes: Answer is c.

## Slide 50
Which file format is best in an application that requires high-speed streaming?
  ASCII
  Binary
  TDMS
  LVM
Lesson Review
Notes: Answer is c.

## Slide 51
Which file format is best in an application that requires high-speed streaming?
  ASCII
  Binary
  TDMS
  LVM
Lesson Review
Notes: Answer is c.

## Slide 52
Recognize the benefits of sequential and state-based algorithms and apply techniques in LabVIEW to enforce sequential or state execution.
Using Sequential Programming
Using State Programming
State Machines
Lesson 10
Using Sequential and State Machine Programming

## Slide 53
A. Using Sequential Programming
Use dataflow to ensure sequential execution of nodes.
Why Use Sequential Programming?
Flow-Through Parameters
Sequence Structures
Error Case Structures

## Slide 54
Why Use Sequential Programming?
A. Using Sequential Programming

## Slide 55
Flow-Through Parameters
A. Using Sequential Programming

## Slide 56
Sequence Structures
Sequence structures are a structure with frames, where each frame executes in order.
A. Using Sequential Programming

## Slide 57
Avoid Overuse of Sequence Structures
Cannot stop the execution in the middle of a sequence.
A. Using Sequential Programming

## Slide 58
Error Case Structures
A. Using Sequential Programming

## Slide 59
B. Using State Programming
Describe the functionality represented by a state transition diagram.
Why Use State Programming?
State Transition Diagrams

## Slide 60
Why Use State Programming?
Change the order of a sequence
Repeat an item in sequence more often than others
Execute only if certain conditions are met
Stop the program immediately
B. Using State Programming

## Slide 61
State Transition Diagram
B. Using State Programming
State—Part of a program that satisfies a condition, performs an action, or waits for an event
Transition—Condition, action, or event that causes the program to move to the next state

## Slide 62
State Transition Diagram
B. Using State Programming

## Slide 63
C. State Machines
Determine when to use a state machine.
What is a State Machine?
When to Use a State Machine?
Building a State Machine
Event-Based State Machine
Simple State Machine Project Template

## Slide 64
What is a State Machine?
C. State Machines

## Slide 65
When to Use a State Machine
Sequential Process
C. State Machines
UI-Driven Process

## Slide 66
State Machine Infrastructure
State Machine Transitions
Building State Machines
Building State Machines

## Slide 67
Course Project Transition Diagram
C. State Machines

## Slide 68
Create a Weather Station application using a state machine design pattern. Practice skills learned throughout this course.
Exercise 10-1
Weather Station Project

## Slide 69
Exercise 10-1
How would you change the diagram to add an Initialize and Shutdown state?
Weather Station Project

## Slide 70
Event-Based State Machine
C. State Machines

## Slide 71
Use the Create Project dialog box to expedite implementing an event-based state machine application.
Simple State Machine Project Template

## Slide 72
Activity 10-1
Refer to the participant guide to answer questions about what you have learned in this lesson and then discuss the answers as a group.
Lesson Review

## Slide 73
When using a Sequence structure, you can stop the execution in the middle of a sequence.
True
False
Lesson Review
Notes: Answer is False.

## Slide 74
When using a Sequence structure, you can stop the execution in the middle of a sequence.
  True
  False You cannot stop the execution in the middle of a sequence.
Lesson Review

## Slide 75
Which of the following are benefits of using a state machine instead of a sequential structure?
    You can change the order of the sequence.
    You can repeat individual items in the sequence.
    You can set conditions to determine when an item in the sequence should execute.
    You can stop the program at any point in the sequence.
Lesson Review
Notes: Answer is a, b, c, and d.

## Slide 76
Which of the following are benefits of using a state machine instead of a sequential structure?
    You can change the order of the sequence.
    You can repeat individual items in the sequence.
    You can set conditions to determine when an item in the sequence should execute.
    You can stop the program at any point in the sequence.
Lesson Review